/***************************************************
* HeeChan Kang
* CSC 431 - AI Robotics
* Assignment One - Inverse Kinematics
***************************************************/

#include <stdio.h>
#include <stdlib.h>
#include <math.h>

void main() {
double x, y, alpha, beta, radius;
double base = 1.0, l1 = 0.8, l2 = 0.8;
double limit = 7*M_PI/8;

/* Take user input for x and y coordinates. */
printf("Enter x-coordinate: ");
scanf("%lf", &x);
printf("Enter y-coordinate: ");
scanf("%lf", &y);

/* Check if the distance of input is out of reach or not */
radius = sqrt(pow(x,2) + pow((y-1),2));

if (y > 0 && radius <= 1.6) {
/* Inverse Kinematics equation derived from class for beta and use	beta to find alpha */
beta = acos( (pow(x,2) + pow(y,2) - (2 * base * y) + pow(base,2) -	pow(l1,2) - pow(l2,2)) / (2 * l1 * l2) );
alpha = atan( -x / sqrt(pow(l1,2) + pow(l2,2) + (2 * l1 * l2 *	cos(beta) - pow(x,2))) ) - atan( (l2 * sin(beta)) / (l1 + (l2	* cos(beta))));
if (alpha > -limit && alpha < limit && beta > -limit && beta <	limit) {
printf("Alpha is: %6.4lf radians or %6.4lf degrees.\n", alpha,	alpha * 180/M_PI);
printf( "Beta is: %6.4lf radians or %6.4lf degrees.\n", beta,	beta	* 180/M_PI);
} else {
printf("The coordinates entered are unreachable due to the	arm's physical limitations.\n");
}
} else {
printf("Invalid input! Either the coordinate is out of reach or the	coordinate is below the ground.\n");
}
}